Practice Writing BPF

Task 1 – write BPFs to capture the following:

- All packets with a TTL of 128 or less for both IPv4 and IPv6
  - tcpdump ‘((ip[0] & 0xF0 = 0x40 && ‘ip[8] & 0xFF =< 0x80) || (ip[0] & 0xF0 = 0x60 && ip[7] & 0xFF <= 0x80))’
- All IP traffic with the DF bit set
  - tcpdump ‘ip[6] & 0x40 = 0x40’
- All packets with the MF flag set and Fragmentation offset result of 31744 / 8
  - tcpdump ‘((ip[6] & 0x20 = 0x20) && (ip[6:2] & 0x1FFF = 0xF80))’
- All TCP packets with destination port equal to or less than 1024
  - tcpdump ‘tcp[2:2] <= 0x400’
- Capture all/only IPv4 packets
  - tcpdump ‘ip[0] & 0xF0 = 0x40’
- Capture all IPv4 telnet and SSH traffic
  - tcpdump ‘((ip[0] & 0xF0 = 0x40) && ((tcp[0:2] = 0x17) || (tcp[0:2} = 0x16)))’
- All TCP packets with ONLY the URG/PSH/FIN flags set
  - tcpdump ‘tcp[13] = 0x29’
- All traffic that contains a VLAN ID of 100
  - tcpdump ‘ethr[14:2] & 0x0FFF = 0x64’
- All traffic that has an IPv4 address of 192.168.36.10
  - tcpdump ‘((ip[0] & 0xF0 = 0x40’) && (ip[12:4] = 0xC0A8240A))’
- All traffic that has a DSCP of 38
  - tcpdump ‘ip[1] & 0xFC = 0x98
- All DNS zone transfers
  - tcpdump ‘tcp[0:2] = 0x35’
- all ARP traffic
  - tcpdump ‘ethr[12:2] = 0x0806’
- All IPv6 next header traffic of EIGRP
  - tcpdump ‘((ip[0] & 0xF0 = 0x60’) && (ip[6] = 0x58))’