TCP Dump Basics

Task 1 – Identify these commands and options:
1. Tcpdump –w capture.pcap = output the tcpdump to the capture.pcap file
2. Tcpdump –r capture.pcap = read the packets from capture.pcap
3. Tcpdump –r capture.pcap port 80 –w http_trac.pcap = input file capture.pcap, sort out the port 80 traffic, then write that to output file http_trac.pcap
4. Tcpdump –q –r capture.pcap | wc –l = input file capture.pcap, quiet mode, then do a linecount
5. Tcpdump –i eth0 host 192.168.0.1 = run tcpdump on the interface eth0 looking for all traffic with that host IP
6. Tcpdump –A –r capture.pcap = input file, print out packets in ASCII
7. Tcpdump –c 10 –r capture.pcap = input file, read until 10 counts
8. Tcpdump –e –r capture.pcap = input file, also prints link-level header on each dump line
9. Tcpdump –n –r capture.pcap = input file, do NOT convert addresses to names
10. Tcpdump –S –r capture.pcap = print absolute, not relative, TCP sequence numbers
11. Tcpdump –v (or –vv or –vvv) = sets verbosity

Task 2 – Identify these filters
1. Tcpdump host 192.168.1.1 or host 192.168.1.2 && port 80 = listens for and collects traffic involving either of the two host Ips and only across port 80
2. Tcpdump src host 192.168.1.1 and dst host 192.168.1.2 = listens for and collects traffic with that specific source and specific destination IPs
3. Tcpdump host www.google.com = print all packets arriving at or departing from google.com
4. Tcpdump src port 80 || src port 443 = print all packets coming from a source port 80 OR 443
5. Tcpdump ether dst host aa:bb:cc:dd:ee:A = print all packets with a destination address of aa...
6. Tcpdump udp port 53 or tcp port 53 = print all packets on UDP or TCP port 53
7. Tcpdump not portrange 1025-65535 = print all traffic from ports NOT in the ephemeral range
8. Tcpdump net 192.168.0.0 /24 = print all traffic from local hosts and the 192.168.0.0 /24 range
9. Tcpdump not net 192.168.0.0 /24 = print all traffic with local hosts and anything NOT in that range

Task 3 – Build the following filters
1. ARP: Create a TCPDUMP filter that will capture all ARP traffic. = tcpdump arp
2. ICMP: Create a TCPDUMP filter that will capture all icmp echo replies coming into interface eth1. = tcpdump -i eth1 icmp[icmptype] ==0
3. TCP: Create a filter that will capture all the closure packets of TCP conversations (both graceful and not) = tcpdump ????

What is Happening Here?

Task 1 – Identify traffic for the packets listed below and answer the following questions:
1) What type of transaction is represented in these packets? MySQL transaction to add traffic
2) Is this normal traffic? Yes?
3) Provide any details you learned from the packets?
- Packet 1 is MySQL traffic that appears to try and insert DOG and GOOFY as an entry for ANIMAL and NAME in a database.
- Packet 2 is also MySQL traffic that appears to provide an OK response

Funny Traffic
Task 1 – Based on the raw data for sample 1, or pcaps, answer the following questions:
1) What is anomalous about this traffic? - It appears to be a Xmas Tree scan from 192.168.47.132 to 192.168.47.1.
2) How could traffic like this be used in an exploit situation? - If the port is closed on the target system, it will respond with an RST. If the port is open, it will not respond. So the exploiter can scan for open ports by parsing out which ports didn’t reply.
3) Is this something you can defend against? How? - Yes, you can minimize unnecessary services and use TCP Wrappers or PortSentry type software to detect and just drop requests from these IPs after a certain number of port requests.

Extracting Files
Task 1 – using the HTTP-file-extract pcap, practice file extraction
- extract a single image from the FTP pcap (pantheon.jpg)
- Googled the hex string for jpeg
- CTRL+F – searched the hex value
- selected one of the ftp data packets, right click, follow tcp string
- saved the RAW output of that stream to a file
- displayed the file via cmd line
- extract any image from the HTTP pcap
- Open the HTTP pcap
- File → Export → HTTP
- selected Packet 942 – young girl with full of bags
- click save, save that to a location on the local drive, display that file via cmd terminal